## Slide 1
Domestic Service Robot:
Basic Coffee Preparation
Assignment D2-V1 Classical PDDL and PDDL+
Richard Albert King Mechoda
MSc Robotics Engineering, University of Genova
Artificial Intelligence for Robotics II

## Slide 2
Problem and solution
The problem
- A fixed manipulator must prepare a cup of coffee in a kitchen
- Required sequence:
  - obtain the empty cup
  - fill it with water
  - add coffee powder
  - brew with the coffee machine
- Constraints:
  - static kitchen, fixed object positions
  - one object handled at a time
- Q1: classical PDDL, two instances with valid plans
- Q2: PDDL+, cooling process, cold event, timing
The solution
- Cup contents modelled as a chain of states; recipe order comes from action preconditions
- Tap, dispenser and machine are location capabilities; only the cup is grasped
- grasp and place are explicit actions on a one-slot gripper
- PDDL+: temperature fluent, autonomous cooling process, event that makes cold coffee unusable
- Checked with a real planner:
  - Q1 with pyperplan, plans of length 3 and 9
  - Q2 with ENHSP, fast delivery solved, slow delivery unsolvable
Richard Albert King Mechoda
2 / 7

## Slide 3
Q1: classical PDDL model
Ordering comes from preconditions, not from a script
Object states form one chain
(empty ?c) -> (has-water ?c) -> (has-powder ?c) -> (coffee-ready ?c)
- Stations are capabilities of locations: is-water-source, is-powder-source, is-machine. Only the cup is grasped.
- grasp and place are explicit; every station operation needs the cup placed there with the gripper free
How preconditions force the order
fill-water needs (empty ?c) only an empty cup can be filled
add-powder needs (has-water ?c) powder strictly after water
brew-coffee needs (has-water ?c) and (has-powder ?c)
Richard Albert King Mechoda
3 / 7

## Slide 4
Q1: instances and plans
Same domain, only the initial state changes the difficulty
Simple: one counter does everything
(fill-water cup1 counter)
(add-powder cup1 counter)
(brew-coffee cup1 counter)
pyperplan: plan length 3
Complex: separate stations, cup on a shelf
(grasp cup1 shelf)
(place cup1 water-source)
(fill-water cup1 water-source)
(grasp cup1 water-source)
(place cup1 powder-dispenser)
(add-powder cup1 powder-dispenser)
(grasp cup1 powder-dispenser)
(place cup1 coffee-machine)
(brew-coffee cup1 coffee-machine)
pyperplan: plan length 9
- Planning difficulty is in the structure of the instance, not in the actions
Richard Albert King Mechoda
4 / 7

## Slide 5
Q2: PDDL+ model
The world changes even when the robot does nothing
Process: continuous cooling
(:process cooling
:precondition (coffee-ready ?c)
:effect (decrease
(temperature ?c) (* #t 1)))
Event: fires by itself at the threshold
(:event coffee-got-cold
:precondition (and (coffee-ready ?c)
(<= (temperature ?c)
(drinkable-temp)))
:effect (and (not (coffee-ready ?c))
(spoiled ?c)))
- Brewing and delivery take time. ENHSP has no durative actions, so each becomes start action, clock process and completion event.
- Delivery completes only if the coffee is still hot when the hand-over ends
start-brew -> brewing-process (clock) -> brew-done at t = 5: temperature := 90
Richard Albert King Mechoda
5 / 7

## Slide 6
Q2: timing decides plan validity
Two instances, identical except one number: delivery-time
delivery-time = 10 -> Problem Solved
0.0 fill-water, add-powder,
start-brew
5.0 [brew-done: 90]
grasp, start-delivery
15.0 [delivery-complete ~80]
goal (served cup1) reached
delivery-time = 70 -> Problem unsolvable
hot window: 90 -> 40 at 1 per unit
= 50 units < 70 needed
coffee-got-cold fires in transit,
delivery-complete can never trigger
ENHSP: "Problem unsolvable"
- The planner even found a loophole in the first model: it put the cup back in the machine mid-delivery and re-brewed the spoiled coffee
  - fix: place forbidden while delivering, spoiling made irreversible. A model must encode all its invariants.
Richard Albert King Mechoda
6 / 7

## Slide 7
What I learned
- State predicates are causal milestones, not physics. Anything left implicit is something the planner can exploit.
- Correct ordering needs no script: preconditions alone give the 3-step and 9-step plans.
- PDDL+ changes the game: processes run without the planner, events fire at thresholds, and waiting is no longer free.
- One duration value flips an instance from solvable to provably unsolvable. That is timing affecting plan validity.
- Practical notes: ENHSP has no durative actions, reserves the name at, and discretises the dynamics with a 1-second step.
Repository: github.com/albertrichard080/D2-V1-Domestic-Service-Robot-Basic-Coffee-Preparation
Richard Albert King Mechoda
7 / 7